HOW TO SET INSTRUMENT HEIGHT AND SET OUT LEVELS WITH THE ELTAR55

The EltaR55 can be used to set-out or survey levels.

The height of instrument can be set:

- When you select Polar/Detail Points or Stake Out you are asked to confirm the station point and the reference direction and then you are can enter the reduced level of the station (Zs) and the height of instrument (Ih).

- Or by selecting Stat. In Elevat. From the Co-ordinates menu.

When you do 2 above you can backsight to a point for which the level only  (not the X,Y co-ordinates) are known.  Proceed as follows:

Select Stat. In Elevat. From the Co-ordinates menu.

Select Stat.

Input

Input Reduced Level of backsight point

Input instrument height

Input target height

Sight on prism & measure point

Press Yes to accept.

Then, after stationing, when you go to Polar-Detail Points or Stake-Out, accept the station information, the reference direction, and the height information and turn Z on instead of off , which is the default.