HOW  TO  DO A SURVEY AND SET OUT POINTS WITH THE ELTA S SERIES ONE-MAN OPERATION

This tutorial will show you how to survey and set out with the Elta S instrument and the Reclink.  It takes approximately  1 hour.

# You will need:

- Charged Elta S,  tripod

- Charged Reclink,  charged radio,  prism pole, cable Reclink-radio

- Station point with known co-ordinates (may be 1000,1000,100)

- Backsight point

- Survey area with features

- Set up the instrument on the station point, level it and press the PWR button.

- When the display shows the Zeiss screen, with ( STARTEN  press  ESC (do NOT press ENTER)

- Display will show level vials press ESC

- When main menu shows select 8 Configuration, and 6 Remote Control

- Press F8 Conn and ENT

- Display will show ESC TO CANCEL.  Do NOT press ESC

- On the prism pole, connect the prism cable to the radio and the radio to Reclink

- Turn on the radio,  turn on the Reclink

- Display:	Husky FS3 – Press any key

- Reset the Reclink by holding both the Shift keys (the up-arrow either side of the number pad)  and holding down the red ON key for 30 seconds, until you here a beep

- Turn on the Reclink

- Select 1 Zeiss S-series (if you don’t select it, it defaults to this automatically)

- Black screen comes up with ‘Suche Elta S..’, wait for it to disappear

- When the black screen clears, the Select 1 Zeiss S-series  screen flashes up momentarily and then the Main Menu for FM700 comes up.

CHECKPOINT 1:	At this stage the instrument is set up over a station point awaiting for instructions.  On the radio the Green (Power) and Red (Link) lights are lit, and the Reclink is showing the Main Menu, with FASTMAP 700v2.0    ZEISS S10/S20 on the top line.

- Select Job Manager…New Project and enter a project name e.g. SURVEY1.  Note the screen will automatically show the date & time and the scale factor of 1.000000.  Enter a description e.g. TEST SURVEY

- Press enter until you see Project Created

- Select 6 New Job and enter the job name e.g. TEST1, surveyor, and start point no. 1.  Press Enter until you see Job TEST1 created

- Esc

- Select 3 Stn.Control…InstrumentSetup…Enter

- You are prompted with a Stn.No. 9001.  Enter a station name: e.g. STNA, press Enter and enter Easting (1000.000), Northing (1000.000), Level (100.000) and press Enter

- When prompted for an RO Stn press the down key and enter a bearing 0°0’0”, enter an instrument height (e.g. 1.6) and a target height (e.g. 1.5) and press enter

Message: Sight RO/BS and Press [Enter]

- Stand with the prism in the 0°0’0” direction and press Z.

Instrument will search and find prism,  Display will show SEARCHING

- Press Enter

- Display then shows E, N, H of station point and direction is 0°0’0”  with message Enter to accept.  Press Enter

- Display returns to Menu

- Press ESC

Checkpoint 2: You have now completed the stationing of the instrument and told it that it is stationed on 1000,1000,100 and given it a reference direction 0°0’0”

- Select 2 Detail Survey…2 Data Record

Display shows blank spaces 1 – 10 and message Buffer Empty

This is the main survey screen

- Press Enter and the feature code dialogue box comes up

Enter a name for the feature code e.g. SPOT

Enter type e.g. POINT

Enter feat. E.g. POINT

If the feature is a line e.g. KERB change the type to STRING or SMOOTH (use ←→ to scroll through options).  The line style can be change using type

- Press W (find left) or Z (find right) to prompt the instrument to find the prism and Enter to record a measurement

The display will show the E, N, Z of the point

- Continue to record point/lines/features in this way.

- The target height can be changed using F4 DATA

SETTING  OUT

We are going to use the same points that we have surveyed to set out.  If you have taken down the instrument it will be necessary to restation as in steps xxxxxx to setup the instrument.

- Go to the Main Menu which should show Job Manager in the top left hand position.

- Select 4 Setout…8 Setout Manager…0 SO from survey

Display:	Current File: NO FILE

Create File:  enter here the name of a file e.g. TESTSO1

- Press Enter

- ESC

- 2 Setout Coords

Display:	TESTSO1

Code:	press enter, ALL, enter

Range:	press enter

PtNum:	Enter starting and end point number e.g. 1 to 3

- Press Enter

- Display comes up with setting out point detail

Message: Turn to bearing xxxxxx and press space

Do NOT DO THIS

- Press S

- Scroll down screen until you come to 1-man-operation

Message: Press <Space> and follow arrow

- Press Space & follow arrow

When you come with in 2m of point you get a bullseye screen that shows a dot where the point is and a circle where the pole is.   You need to get the point inside the circle.  When you get nearer there will be a square and a circle.  You should get the circle inside the square.