# HOW TO SCALE & POSITION AN AUTOCAD DRAWING

# TO SAVE AN AUTOCAD DRAWING AS A .DXF FILE

- Load the drawing in Autocad

- File…Export

- Type in name of .dxf file

- SaveAs type: Autocad R14.DXF

TO MOVE THE .DXF DRAWING IN AUTOCAD TO 0.00 & CHANGE FROM mm TO m

## MOVE

- Open the Autocad drawing

- Notice that the base point co-ordinates are 1000000,1000000.  We will move that point to 1000,1000

- Type ‘Move’ on the command line <CR>

- Select Objects: All <CR>

- <CR> again

- Base point of displacement: Snap to point above 1000000,1000000

- 2nd Point of displacement: 1000,1000 <CR>

- Drawing will move to new base point, Zoom…Extents to see it.

## SCALE

1	Notice that the scale is incorrect: all dimensions are in mm.   To change to m:

- Type ‘Scale’ on the command line, <CR>

- Select Objects: All <CR>

- <CR> again

- Base Point: Snap to 1000.000, 1000.000

- ScaleFactor/Reference:   .001 <CR>

- Drawing will shrink about this point to the new size.  Zoom in for detail

## ROTATE

Drawing may need to be rotated to align with a particular element.

- First find the angle of the element that you want to align.  Find List in the Tools menu or type it on the command line.  Click on the element and display will show the angle to the XY plane.  This is the rotation angle or you may have to subtract it from 360º

- Type Rotate on the command line

- All

- <CR>

- Enter angle