### HOW TO SET-OUT WITH THE TC(R)307

This datasheet will show you how to use the TC(R)307 total station to set out points.

#### You will need:		TC(R)307 with charged battery

Tripod

Co-ordinates of fixed points on the ground (A, B)

Co-ordinates of  points to be set out (C, D, E….)

Reflector for TC307

##### Set up the total station on point A and turn on the instrument

- The level vial display will show on screen and the laser plummet will be activated.

- Using the laser plummet set the instrument over the point and level it.  OK will be hightlighted on screen.  Press ENT (red button on bottom right hand corner)

- If the instrument is not levelled properly the level display will flash during use.  Relevel the instrument and press ENT.

- Display should now show PtID

#### Starting a new Job

##### Press PROG button

- Highlight SETTING OUT and press ENT

- Highlight SetJob and press ENT

- Highlight NEW and press ENT

- Note: If ‘All jobs occupied’ see Delete Jobs on separate datasheet HOW TO DOWNLOAD SURVEYS FROM THE TC(R)307

- Press the right arrow button and the number scroll bar appears in the right hand position.  Scroll through the numbers to select what you require.  If you want letters press the SHIFT button.  Select the letter you want.  Use the left arrow to position the scroll bar where you want it.  When you have selected the letter/number required press ENT and move to the next position.

- Highlight Oper and select an operator number or letter in the same way

- When complete highlight SET and press ENT

Stationing on a point

- When the new job is set above the display shows the  SETTING OUT screen with SetJob ticked and SetStation highlighted.  Press ENT

- Enter a name for the station e.g. A and press ENT

- Screen will show ‘Point not found’ and display shows NEW POINT screen.

- Enter the co-ordinates for the station point using the arrow buttons

- Highlight OK and press ENT

- Display shows SET STATION screen with the point and values you  have just entered.  The height of instrument is highlighted, enter the height of instrument above the station point.  If the values for the station co-ordinates are correct highlight SET and press ENT

Set Orientation

- Display will show SETTING OUT screen with SetJob and SetStation ticked and SetOrientation highlighted, press ENT

- DO NOT ACCEPT THE DEFAULT BACKSIGHT BEARING (Bsgt Brg.) BY HIGHLIGHTING SET AND PRESSING ENT EVEN IF IT APPEARS CORRECT.

- You can set the orientation by setting Hz=0 (22) or by backsighting onto known co-ordinates (23):

- To set Hz=0, point the instrument in the 0º direction, highlight Hz0 and press ENT.  Highlight SET and press ENT or

- To backsight onto a known point highlight COORD and press ENT.  Enter the name of the backsight point, press ENT, display will show point not found and NEW POINT screen will appear.  Enter the co-ordinates of the new backsight point, highlight OK and press ENT.  Sight on the backsight point, highlight SET and press ENT

- Display will show SETTING OUT screen with START highlighted, press ENT

#### Setting Out

- Display will show 2D SET OUT screen with the point name highlighted.  If you have entered the points into memory (see below) you can now scroll through them using the left/right arrow button until you find the one you want to set out.

- If you have no points entered, use the up arrow button to highlight PtId,  enter the name of the point you want to set out (use the Ins button), and press ENT.

- Screen will ‘Point not found’ and the NEW POINT screen.

- Enter the co-ordinates of the set out point, highlight OK and press ENT.

- Display shows 2D SET OUT screen:

Dist:  Is the distance to the point

dHz: Turn the instrument until this angle is 0º0’0”

- Align the prism with the line of sight and press the DIST button.

dHD shows how far the prism needs to go out (+ve) or come closer (-ve)

- Continue to move out and closer with the prism until dHD is 0.  This is the position of the set out point

- To set out further points repeat from 33 above.

- To set out levels as well as horizontal position you need to do the following in addition to above:

- When stationing you must enter the reduced level of the station point (H0) and the height of the instrument above the station point (hi)

- When stationing & orientation is complete highlight START and press ENT.

- Display will show 2D SET OUT as in 33 above.  Change to 3D SET OUT by pressing the Shift button followed by the down arrow button.

- Highlight hr and enter the height of the reflector

- Select point to be set out as in 33 and continue as in 34-38.

- dH is the error in height setting out.

- Set out further points as from 44.

Entering setting out points into memory

- When you turn on the instrument display shows PtId in the top left hand corner

- Press SHIFT button followed by PROG button

- Highlight Data Manager and press ENT

- Highlight View/Edit Data and press ENT

- Highlight Fixpoint and press ENT

- Highlight Job and use the arrow button to scroll to the job required

- Highlight NEW and press ENT

- Enter Point Id using the arrow buttons (Shift for alpha characters). Enter co-ordinates, highlight Save and press ENT

- Continue until all points are entered.

- Note: Points can be much more easily entered using the Leica Survey Office program, where they can be entered in tabular form directly from the keyboard and easily uploaded to the instrument.

- Insert the CD into your drive, wait for Autorun (or click on Setup on the disk) and follow the installation instructions.

- Start the program and click on Coordinate Editor

- Click on File and New and enter a filename

- Enter Point Id & co-ordinates

- Click on File and Save As and save the file.

- Connect the PC to the instrument, click on Data Exchange Manager

- Screen shows Windows Explorer type screen with the instrument jobs on the left and your PC folders on the right.

- Locate your saved file and drag it across to the job on the instrument

- The setting out coordinates are then copied to the instrument

#### Free Stationing

- Go to main screen with PtId in the top left hand corner.

- Press PROG button

- Highlight Free Station and  press ENT

- Set job as before

- Start is highlighted, press ENT

- Enter a name for the point you are stationing on

- Enter the height of the instrument hi above the station

- Highlight OK and press ENT

- Display shows FREE STATION 0/

- Enter the name of the 1st backsight point

- Screen shows co-ordinates of the 1st backsight point, to confirm highlight OK and press ENT

- Sight on the backsight point, highlight MEAS and press ENT

- Enter the name of the 2nd  backsight point

- Screen shows co-ordinates of the 2nd  backsight point, to confirm highlight OK and press ENT

- Sight on the backsight point, highlight MEAS and press ENT

- Highlight CALC and press ENT

- If coordinates appear correct highlight SET and press ENT

- Press PROG button to start setting out

- DO NOT SELECT Set Station or Set Orientation.  Highlight Start and press ENT