### HOW USE THE ML3 FOR GRADES

This datasheet will show you how to use the ML3 rotating laser to set grades on sewer lines.

#### You will need:		ML3 with charged battery

HS2 detector on staff  (2x1 timber or similar)

Tripod

Fixed points on the ground (A, B), proposed manholes for sewer

##### Set up the laser at or near to point A.

Note: It is not necessary to set the laser over point A

##### Measure the distance the laser is offset from A.

B

Staff

OFFSET

A

ML3

- Hold the staff at B offset from the sewer line by the same distance.

- Slacken the instrument screw on the tripod and rotate the ML3 until the sightline across the top of the laser is pointed exactly at the staff.

- Check that the grade pointer on the side of the ML3                 is pointing the same way that the sewer is rising/falling.  If it is not rising/falling the same way as the sewer rotate the laser 180° and line it up with the staff again.

- Turn on the laser

- Set the grade for the laser (e.g. 1 in 56 = Laser reading 100/56=1.786, or see datasheet 4 for more information)

- Laser should relevel to the set grade and start to rotate.

- Set the staff on the invert level of manhole A.

- Slide the detector up/down the staff until it picks up the centre of the beam.   Clamp the detector at that point.

- As you lay each pipe put the bottom of the staff on the invert of the pipe and the detector will indicate up/down/on grade.

- If you wish to monitor the excavation level slide the detector up the staff by the depth of formation level below invert (e.g. 40mm pipe thickness + 100mm pipe bedding = slide detector up staff by 140mm and clamp at that point)

NOTE: the above procedure can be used for other grades e.g. road surfaces (camber not covered), kerblines, single grade pitches etc.