### HOW USE THE ML11x FOR GRADES

This datasheet will show you how to use the ML11x rotating laser to set grades on sewer lines.

#### You will need:		ML11x with charged battery

HS2 detector on staff  (2x1 timber or similar)

Tripod

Fixed points on the ground (A, B), proposed manholes for sewer

##### Set up the laser at or near to point A.

Note: It is not necessary to set the laser over point A

Measure the distance the laser is offset from A.

Staff		B

OFFSET

ML11X		A

- Hold the staff at B offset from the sewer line by the same distance.

- Slacken the instrument screw on the tripod and rotate the ML11x until the sightline across the top of the laser is pointed exactly at the staff.

- Turn on the laser

- Wait for the laser to level up.

- Press the MAN button, MAN should appear in the bottom right hand corner of the display.

- Press the up/down arrow to set the grade.  Plus/positive grades are rising as shown by the grade pointer on top of the laser, see Fig. 2.  Negative grades fall in this direction.

- Wait for the laser to relevel to right grade

- Set the staff on the invert level of manhole A.

- Slide the detector up/down the staff until it picks up the centre of the beam.   Clamp the detector at that point.

- As you lay each pipe put the bottom of the staff on the invert of the pipe and the detector will indicate up/down/on grade.

- If you wish to monitor the excavation level slide the detector up the staff by the depth of formation level below invert (e.g. 40mm pipe thickness + 100mm pipe bedding = slide detector up staff by 140mm and clamp at that point)

NOTE: the above procedure can be used for other grades e.g. road surfaces (no camber), kerblines, single grade pitches, car parks etc.