HOW  TO UPLOAD SETTING OUT POINTS TO THE LEICA TPS1100 SERIES

This tutorial will show you how upload points created by n4ce to the TPS1100 series instrument.

# You will need:

- *.log file of setting out points created by n4ce for Leica logger on your PC

- Leica Survey Office software on PC

- TC1100 series instrument with PC card

- PC cable

- When creating the *.log file using n4ce in order to see the point code on the instrument rather than the point id, swap the point code & point id columns (In co-ordinates folder  in n4ce, l. click on heading of point id column, r.click in column, l.click Swap Code-No)

- Connect PC to instrument using the PC cable

- On instrument select Configuration…CommunicationMode…GeoComOn-Line…Yes

- Start Leica Survey Office on PC and click on Data Exchange Manager

Checkpoint 1:		PC  display should show COM1/2 with TPS1100 on left hand side and PC drives on right hand side.

- Expand the display on the left hand side by clicking on the + sign at COM1/2, expand memory card and it should show a GSI folder

- Locate *.log file on RHS and drag to the GSI folder

Checkpoint 2:		Display should show window ‘Uploading Data’ and a progression bar 0-100%

- On instrument EXIT…BACK…BACK to Main Menu

- Select 4 Data Conversion

- Press F2 – CONF

- Set the following settings:

Search extens.:  		LOG

Header lines:		0

Default extens.:		GSI

- Press F3 – ASCII

- Set the following settings

Separator			Space

ID Pos			1

East Pos			2

North Pos			3

Height Pos			4

Pt. Code Pos		5

Attrib 1 Pos		6

Attrib 2 Pos		7

- Press OK

- Press OK again

- Set the following settings:

Source Path:			A:\GSI\

Source file					Select file

Format				GSI

Output Path			A:\GSI\

Output File					As prompted

Format				GSI8 (8Char)

17.	Press OK again

- Press F1 – GO

Checkpoint 3: 		Display should show progression bar and Completed! when points are converted.

- Press EXIT

- Highlight Data Job Management and press <CR>

- Highlight uploaded file and press <CR>