HOW  TO DOWNLOAD A SURVEY FROM THE LEICA TPS1100 SERIES

This tutorial will show you how to download a survey from the TPS1100 series instrument.

# You will need:

- Survey carried out on the TPS1100 instrument stored in the memory card.

- Leica Survey Office software on PC

- TC1100 series instrument with PC card

- PC cable

- Connect PC to instrument using the PC cable

- On instrument select Configuration…CommunicationMode…GeoComOn-Line…Yes

- Start Leica Survey Office on PC and click on Data Exchange Manager

Checkpoint 1:		PC  display should show COM1/2 with TPS1100 on left hand side and PC drives on right hand side.

- Expand the display on the left hand side by clicking on the + sign at COM1/2, expand memory card and it should show a GSI folder

- Locate the measurement GSI file and drag to a folder on the RHS e.g. Temp Survey

Checkpoint 2:		Display should show window ‘Uploading Data’ and a progression bar 0-100%

6.	The .GSI file should open in n4ce