HOW  TO SURVEY WITH THE TC407

This tutorial will show you how to use the TC407 total station to set out points

# You will need:

- TC407 with charged battery

- Reflector

- Tripod

- Co-ordinates of fixed points on the ground (A,B)

- Set up the total station on  point A and turn on the instrument

- The level vial display will show on the screen and the laser plummet will be activated.  If the level display does not show press FNC button followed by F1.

- Using the laser plummet set the instrument over the point and level it.  OK will show in the bottom right hand corner. Press F4

- If the instrument is not levelled properly the level display will flash during use.  Relevel the instrument and press F4

- Display should now show Main Measure 1/4

Starting a New  Job

Note: At any stage you can go back one menu step by press the ESC button

- Press Menu button

- F1 Programs

- F1 Surveying

- F1 Set Job

- F1 New

- F1 Input

- F4 followed by F1, F2, F3, or F4 to select letters for the job name.  Press ( (red button in the bottom left hand corner) when complete

- Enter Operators name and remarks in the same way.

- When all entries complete press F4 to set the job

## Stationing on a point

- When the new job is set above the display shows the SURVEYING screen with Set Job ticked.

- F2 Set Station

- F1 to input name of station, enter name

- F4 for new station

- F1 to enter the co-ordinates for the station point

- F4 to save point to memory

- F4 to set instrument height and set station.  Note for 2D setting out height of instrument is irrelevant.

Set Orientation

- Display shows SURVEYING screen with Set Job and Set Station ticked.

- F3 to  Set Orientation

- You can set orientation by Manual Angle Setting F1 or by backsighting onto know co-ordinates F2.

- To set an angle press F1, point the instrument in the required direction, press the right arrow key and enter the angle.   Press ( when complete and F3 to set the angle.  Or

- To backsight onto a known point press F2 followed by F1 to input the backsight point name.  F4 and F1 INPUT to enter the co-ordinates of the point.  F4 to save the point to memory.

- Sight on the backsight point and press F1 to measure the distance.  Press the PAGE button and display shows error in distance d◢

- If the error is acceptable press F2 to set orientation.

Surveying

- Display will show SURVEYING 1/3 with PtID highlighted.  To enter a value for the point id press F1 Input.

- Highlight hr and enter the reflector height.

- Press F4 for next menu.

- Highlight Code and use the left arrow key followed by F1-F4 to enter the point code.

- Sight the prism on the point and press F3 ALL

- Note: To ensure recording of surveyed point you must press F3 ALL button, it is not sufficient to press F3 REC button.

- Continue to sight points, change the code and press F3 ALL button to continue surveying.

- Display shows angle and distance to each point. To see the co-ordinates of a surveyed point press the PAGE button until E N H is showing and press the F2 DIST key.

## Codelists

- Codelists can be accessed while surveying by pressing the F2 Code button at 32 above.  You can then scroll through the list using the left/right arrow button and set the required code using F4 Set.

- Codelists are more easily set up on the PC under Leica Survey Office and then copied over to the instrument.  If you wish to use a new code in the field you can enter it as described above, however, it is not entered in the codelist.  You can also set up a codelist on the instrument as follows:

- From Main Measure 1/4 press Menu button followed by F4 File Management

- F4 Codes

- F1 New

- F1 Input followed by F1, F2, F3, or F4 to select letters for the code.

- F4 Save

# Comments

d◢

d◢▏