### HOW TO DOWNLOAD SURVEYS FROM THE TC407

#### Download Jobs

- Connect the instrument to the computer using the download cable.

- Start Leica Survey Office on your PC.  Click on Data Exchange Manager.

- A Windows Explorer screen will load with the instrument on the left and the PC drives on the right.

- Click on the + sign to the left of the instrument in the left hand window and then on the + to the left of Jobs and then on the + to the left of the job you want to download.

- Each job will have FixPoints (Station points) and Measurements (Surveyed points)

- Drag the Measurements from the left hand window to an appropriate folder in the right hand window on your PC

- The ‘Data Download’ dialogue box will appear

- Enter a filename for the information in the left hand space

- Select a format in the right hand space:

- LDDxyz =	Land Development Desktop format in X,Y,Z.  This file can be viewed in Notepad or Excel

- DXF3D = Autocad DXF file in 3 dimensions

- IDEX =	This format contains all the survey information, can be read in Notepad

- GSI = 	Leica’s own format, not suitable except for Leica software.

- GSI_4ce = N4ce format.

- CSV6 = N4ce format

- Other formats are available.  To load formats see below.

- When downloading is complete the screen will revert to Windows Explorer type screen.

#### Loading formats

- Get the format in a .frt file and load it onto your PC or a floppy diskette.

- Start Leica Survey Office and Data Exchange Manager as above

- Click on the + sign to the left of the instrument in the left hand window and then on the + to the left of Formats

- Locate the .frt file in the right hand window on your PC

- L-click and drag the format from the right hand window pane to the format folder on the instrument

- The dialogue box will prompt for a name, give it one, OK.

- Transfer will take place.

- Now when you download a survey you may select this format for your download information.