HOW TO REDUCE A SURVEY IN n4ce

This procedure has not been tested

This datasheet will show you how reduce a survey downloaded into n4ce.

# You will need:

- N4ce Lite software on PC

- Downloaded survey.

- L-click on Stations

- Type in Name, E,N,H of the 1st station and it will blue out

- L-click on station folder under observations

- If 1st line is backsight angle only change code to name and number to –88

- If last line is forward sight change code to forward station name and change number to –99

- Both should now be dark yellow

- In next station folder change 1st backsight code to station name and number to –99

- R-click on folder and L-click on reduction.  There is a list of station names matching the folder names and their status should be ‘known’ or ‘derivable’

- Unclick ‘Gen. Report’, click ok

- R-click Model, New, normal, form dtm, test? Tab survey and available to selected.