### HOW TO USE DOUBLE PENTAPRISM TO SET OUT A RIGHT ANGLE

This tutorial will show you how to set out a right angle with the double pentaprism.    It takes approximately  5  minutes.

You will need:

- 2 fixed points on the ground, A & B, as a base line

- 3 No. Ranging rods.

- Place one of the ranging rods at point B

- Hold the pentaprism over point A, use a ranging rod to steady the pentaprism

- Sight point B over the top and through the gap in the prisms.

- Have a partner move the 3rd ranging rod at point C to the left or right until the image of the ranging rod at point C aligns with the ranging rod at point B, fig 2.