HOW  TO SURVEY WITH THE NTS302B TOTAL STATION

This tutorial will show you how to survey points with the NTS302B total station, including stationing, setting backsight angle to 0°, and surveying points.

It takes approximately  1.0 hours

Also included are  Moving to a forward station, Backsighting to a known point, and Downloading to a PC (CD, Download Cable & PC required).

# You will need:

- NTS302B total station with charged battery

- Tripod

- Prism & pole

- Staffman to hold the prism

- Points on the ground on which to station STNA (1000,1000,100) and STNB

- Points to survey 1, 2….

CONFIGURATION – Set these configurations each time at power up

- Turn on the instrument, display will show V OSET TURN.  Tilt the telescope up/down and display will show V, HR

- Press STAR button to left of On/Off button, display will show “Contrast Adjustment”

- Set Compensator: F2:TILT

- F1:X-ON

- F4:YES

- Set Prism Constant: F3:S/A

- F1:PSM, set to -30

- Set Pressure & Temp: PRES should be in range 995-1015, PPM should be in range 0 to -11

- ESC twice

STATIONING

- MENU button.

- F1:DATA COLLECT

- Select a file: Since there are no files in the instrument we must input a file: F1:INPUT.  (Later when there are a number of files in the instrument you may select by F2:LIST)

- We will call our file TEST, press the following keys:
1 – F2= T
8 – F2= E
1 – F1= S
1 – F2= T
F4:ENT to complete the input

- Display then shows the DATA COLLECT menu

- It is important to check the save configuration before starting to survey.  
Press F4:P(

- F3:CONFIG

- F3:SAVE CONFIG

- F1:YES and F4:ENT

- ESC and F4:P(

- Display again shows the DATA COLLECT menu, select F1:OCC. PT. INPUT

- F1:INPUT the point number Pt#: STNA, point code P.Code: ST, and instrument height – measure from dot on LHS of instrument to top of station (e.g  1.530).

- You can scroll up and down the display using the arrow keys to the right hand side of the display.  Press F4:ENT when finished entering data

- F3:OCC

- F3:NEZ

- Input the following co-ordinates for STNA:
N: F1:INPUT, 1000, F4:ENT
E: F1:INPUT, 1000, F4:ENT
Z:F1:INPUT, 100, F4:ENT

- F4: NOTE and F4:YES and the station point information is recorded to the instrument

CHECKPOINT 1:		Display should show the DATA COLLECT menu again

- Select F2:BACKSIGHT to orient the instrument

- Point at STNB or a well-defined point to orient the instrument and  F2:OSET, F4:MEAS, F1:VH and F4:NOTE to set the backsight direction.
See below for orienting to a backsight point.

- F3:MEAS

- F1:INPUT and input a PT#, F4:ENT

- F1:INPUT and input a point code PCODE e.g. WL (for wall), HG (hedge), KB (kerb), MH (manhole) etc.  You can enter more than two characters but traditionally only two have been used to save key input time. F4:ENT

- F1: INPUT and enter the reflector height R.HT.

CHECKPOINT 2:		Display should show  PT#: (say 1), PCODE (say WL), R.HT: (say 1.3)

SURVEYING

- Set the reflector on the first point to be measured and point the telescope cross-hairs at the centre of the prism.  F3: MEAS

- F3:NEZ

- Display will show the co-ordinates of the point, F4:NOTE to record the point co-ordinates and information.  The PT# will increment automatically.

- Move to the next point (change PCODE if necessary) and  F4:ALL

- Continue to record points in this way until all points are surveyed.

- If battery goes dead during survey, or you turn off the instrument, it is necessary to re-station (Points 20-28) on your present station to ensure correct co-ordinates

- To check that co-ordinates are being recorded, press ESC button back to MENU and  F3:MEMORY MGR, followed by F2:SEARCH, F1:MEAS DATA, F4:ENT and F2:LAST DATA
It is not necessary to restation after checking co-ordinates, to return to surveying  ESC x 4, F1:DATA COLLECT, F4:ENT and F3:MEAS and continue surveying.

MOVING TO A FORWARD STATION

- Survey the forward station point (STNB) as a normal point as above.

- Move the instrument to set up on the forward station STNB.

- MENU key

- F1:DATA COLLECT, and F4:ENT to accept file

- F1:OCC. PT# INPUT

- F3:OCC

- F2:LIST

- Scroll through the list until the arrow is opposite the station point STNB,  F4:ENT, and F1:YES

- Enter PCODE

- Enter instrument height above the station point

- F4: NOTE, F4:YES

BACKSIGHTING TO A KNOWN STATION

- After we have moved to a forward station we want to orient to a known backsight point.

- F2:BACKSIGHT

- F3:BS

- F2:LIST
 (or F3:NEZ  and enter the co-ordinates if there are no points in memory, go to 56)

- Scroll through the list until the arrow is opposite the backsight point,  F4:ENT, and F1:YES

- Enter a new PT#

- Enter PCODE

- Enter reflector height R.HT

- Set the reflector on the backsight point and point the telescope cross-hairs at the centre of the prism.  F3: MEAS

- F3:NEZ

- F1:MEAS

- Display shows the co-ordinates of the measured point and F4:NOTE

- Continue to survey F3:MEAS

DOWNLOADING TO A PC

- Connect the cable to the PC and the instrument.  Check which COM port the cable is attached to, usually it is COM1

- Start the download software on the PC by double-clicking on the file 
NTS300-COM.EXE and the software will load.

- Click Comm/Parameter and setting should be
COM1, 8, 1, None	Click OK

- Click Comm/DownloadData/OK

- On instrument  MENU key

- F3:MEMORY MGR

- F4:P( twice

- F1:DATA TRANSFER

- F1:SEND DATA

- F1:MEAS DATA

- F4:ENT

- F4:YES
The point number of the transferred points will show in the bottom left hand corner of the instrument display

- On the PC the point information will display in the NTS300-COM window.

- Click Transform/CASSCoordinate(ENZ) and the information will display in columns of PT#, PCODE, E, N, Z

- Click File/SaveAs add a .nts extension (it is not added automatically) and save the file.