HOW TO USE THE S82 BASE AND ROVER FOR SURVEYING

This datasheet will show you how to set up the base station on a known point and use the rover with the Psion Workabout Pro running Estar software to carry out a survey and download it to your PC

# You will need:

- S82 Base & Rover, tripods, radio

- Psion Workabout Pro with Estar 2.0 software

- Co-ordinates of base station

- 3m measuring tape

Set up base

- Connect radio with aerial to the base and turn the radio on.

- Set radio to channel 1 by pressing the CHANNEL button until 1 shows in the radio display.

- Set up the base station over the known point, connect it to the radio, and turn it on

Checkpoint 1: Immediately after turn-on the base will show

STA	Red

DL

BLU

PWR	Red

After 2 minutes it will show

STA	Blink red at 1 second interval

DL	Blink red twice at 5 sec interval

BLU	Blink red N times every 30 seconds (N=No. of found satellites)

PWR	Red

If display does not show this hold PWR button on base for 3 beeps, followed by 6 seconds, followed by a further 4 beeps, release power button.  Press PWR button again and wait 2 minutes, it should show the display above.

- Turn on Psion

- Start Estar program by double clicking on icon

- Click Job>NewJob

- Enter name for new job, select Copy and click OK

- Select \Job\Test\Test.ini   and click Ok
Note: All parameters (Ellipsoid, Grid Origin, Time Zone, Svs Mask) have been set by copying job from Test.ini

- Connect Psion to base

- Click Set>ComPortSet>Connect by: Cable>Connect
Note: If Psion ‘hangs’, at any stage, you can do a warm reboot by holding the blue and red keys for 6 seconds.  You will need to restart Estar but no information will be lost and you will not need to re-do anything you have done, just continue from where you left off.  Sometimes a Psion window opens behind a current window, to bring it to the front, press blue key and red key together.

Checkpoint 2

Display should show a window with a radio icon in top left hand corner and below window the following:
Pt Id: 1							Status (>4) Base
N:  xxxxxxxxxx					PDOP: < 3
E:   xxxxxxxxxx					HRMS: < 0.020
H:   xxxxxxxxxx					VRMS: < 0.030

- Click Set>RadioSet.  Set Switch to 1 and click Switch, should get Switch Channel ok! after 10 seconds

- Click Read, should get Read Radio ok! after 10 seconds

- Click Close.  Display should show 1 beside radio icon in top left hand corner of window.

- TX light on radio should be flashing at 1 second interval.  If not, click Job>CloseReceiver>Yes, base will shut down.  Press PWR button to start it again and wait 2 minutes.  Display should be as 10 above with 1 beside radio icon, and TX light should be flashing.

Set up Rover

- Put rover on pole and turn it on

- Disconnect Psion from base and put on pole

- Double click on Bluetooth icon (it looks like a chess pawn) in desktop taskbar

- Bluetooth Manger dialogue window will open. Click Scan.

- Double click on T07823494? under Name and Services window will open.  Double click on ASYNC and tick Active.  Note com port number COM? under Port

- Close Services and Bluetooth Manager windows by clicking Ok twice

- Click Set>ComPortSet>InputCom and set it to the number found in 20 above

- Click Connect. Display should return to Estar main screen.

- Click Set>RadioSet.  Set Switch to 1 and click Switch, should get Switch Channel ok! after 10 seconds

- Click Read, should get Read Radio ok! after 10 seconds

- Close Radio Set window

Checkpoint 3: Display should the radio icon in top left hand corner of the window with the number 1 and a power bar showing strength of radio signal.  Underneath the window should be:

Pt Id: 1							Status (>4) Fixed
N:  xxxxxxxxxx					PDOP: < 3
E:   xxxxxxxxxx					HRMS: < 0.020
H:   xxxxxxxxxx					VRMS: < 0.030

The rover should show:

STA	Blink red every second

DL	Blink red every second

BLU	Green

PWR	Red

If not, click Job>CloseReceiver>Yes, base will shut down.  Press PWR button to start it again and wait 2 minutes.  Display should be as shown.  If there is no power bar beside the radio icon, check 14 above.

Surveying

- Click Tools>Correction>Base on Known Point>Next

- Enter co-ordinates of base station (x=N, y=E). Tick Slant>Adjust>Ok
Note: Slant height of base station is measured from top of station to rubber ring on periphery of base, between the white and blue sections.

- Click Survey>Store, enter Pt Id: 2 and code for survey point, Ant.H=2.075 and click OK to save point.

- Continue to survey, point should be Fixed not Float or DGPS and HRMS should be <0.020 and VRMS should be <0.030

- Display should show a sketch of surveyed points

- You can load Save Survey Data screen by pressing the ‘A’ button

- You can set automatic surveying by Set>OtherSet>StoreSet and change Save Type to automatic, and AutoSave to Time or Distance as required.

- You can see a list of surveyed points by pressing the ‘B’ button twice.

- When finished surveying:
Rover: Job>CloseReceiver>Yes
Base: Connect with cable: Set>ComPortSet>Connect and Job>CloseReceiver>Yes
By doing this you can ensure that base and rover units are ready to commence surveying as before.

Downloading to PC

- To download the survey onto a PC click Job>FormatConvert.

- Select Format (e.g Pn,Pc,x,y,h)
Input Filename = File name from 7 above
Output Filename – SD Card = Enter file name
Click OK

- Click Convert and you should get a message “Convert ok, ….”

- Exit

- Turn off Psion, remove battery, lift lever at top of the battery compartment.

- Press forward on card and release, the SD card should pop out.

- Remove card and put it in the card reader.  It only fits one way (“512” facing away from “SKK Card Reader”)

- Put reader in USB of PC, and when Removable Disk dialogue window opens select “Open Folder to View Files”

- Copy files to PC.