### HOW TO USE THE OPTICAL SQUARE TO SET OUT A RIGHT ANGLE

This tutorial will show you how to set out a right angle with the optical square.    It takes approximately  5  minutes.

You will need:

- 2 fixed points on the ground, A & B, as a base line

- 3 No. Ranging rods.

- Place one of the ranging rods at point B

- Hold the optical square over point A, use a ranging rod to steady the optical square.

- Sight point B over the top at the left hand side of the optical square.

- Have a partner move the 3rd ranging rod at point C to the left or right until the image (appearing in the left hand half of the optical square) aligns with the ranging rod B over the top of the optical square (Fig. 2).